## Slide 1
DigDataProcessing project
Objective of the project is the analysis of the data recorded with CAEN digitizer with special signals recognition algorithms
GUI interface allow to monitor data online, and process data on the fly
Raw data from digitizer converted to ROOT TTree format very convenient for analysis with ROOT facility
Calculation of signals amplitude, signal’s time at ½ of amplitude, signal’s front and back length
Time of signal is determined by signal’s front fit with polynomial function power 1 and 3
Special algorithms for different types of signals applied: amplitude, logic NIM, XY coordinate detector’s signals
blackman filter applied to data allow to annihilate 500Mhz noise come from data digitizing
Project’s structure is open to the simple addition of new types of signals and new versions of analysis algorithms
GUI main window: online signal monitoring
No filter
Blackman filter

## Slide 2
A/10
A/10
A/2
Front begin
Back end
Front end
Back begin
Amplitude
Zero level
Time
Front fit
A
Zerol level is mean level out of signal
Amplitude is signal’s extreme
Frond and back edges placed at A/10
Time determined by pol1 (pol3) fit at A/2
Charge is area under signal from Front begin to Back end
Under development
Signal’s peak pol2 fit
Simulation of
Time above threshold (TOT)
Leading edge discriminator (LED)
Constant fraction discriminator (CFD)
Zero level by polynomial fitting
Signal’s gap
Zero level fit